Hardware reduction in FPGA-based compositional microprogram control units

Barkalov A.A.

The University of Zielona Gora, Poland

A.Barkalov@iie.uz.zgora.pl

Titarenko L.A.

The University of Zielona Gora, Poland

L.Titarenko@iie.uz.zgora.pl

Miroshkin A.N.

Donetsk National Technical University, Ukraine

MiroshkinAN@gmail.com

Abstract

The new design method for compositional microprogram control units with code sharing is proposed. The method targets on reduction in the number of look-up table elements in the combinational part of control unit. Some additional control microinstructions containing codes of the classes of pseudoequivalent chains are used for operational linear chains modification. The proposed method is illustrated by an example. The research results for various graph-scheme of algorithms (GSA) are illustrated with the diagrams. Most desirable GSA characteristics for using proposed method were obtained.

Key words – compositional microprogram control unit, graph-scheme of algorithm, FPGA, logic design, LUT.

1. Introduction

A control unit (CU) is one of the important blocks of any digital system [1]. The problem of hardware amount reduction is an important problem connected with implementation of logic circuits of CUs [2]. Peculiarities of a control algorithm to be implemented as well as logic elements in use should be taken into account to solve this problem. In this article we propose a method of this problem solution in the case when a linear control algorithm is implemented using field-programmable gate arrays (FPGA). Peculiarity of FPGA is a very small amount of inputs in look–up table (LUT) elements (not more than 4-6) [3]. It leads to application of the functional decomposition, the number of levels in combinational part of CU increases and therefore, its cycle of time increases too. To decrease this negative effect, it is desirable to diminish the number of variables in logic functions to be implemented [6]. The second feature of modern FPGA is existence of embedded memory blocks (EMB), which can be used for implementing regular parts of a CU [3].

Compositional microprogram control units (CMCU) are widely used for implementation of linear GSAs [6]. Remind that in a linear algorithm there are more than 75% of operator vertices [6]. In case of CMCU, its addressing circuit is implemented using LUT elements, and its control memory is implemented using EMBs. In this article we propose to use the classes of pseudoequivalent operational linear chains (POLC) and the maximal encoding of the collections of microoperations for reduction of code sharing. A control algorithm to be interpreted is represented by a graph-scheme of algorithm (GSA) [7].

2. Analysis of CMCU with code sharing

Let a control algorithm to be interpreted be represented by a graph-scheme of algorithm (GSA) Г [7]. Let this GSA be characterized by the set of vertices  and the set of arcs , where  is an initial vertex,  is a final vertex,  is a set of operator vertices, and  is a set of conditional vertices. Each operator vertex  contains a collection of microoperations , where  is a set of data-path microoperations. Each conditional vertex  contains some element , where  is a set of logical conditions (input signals). A GSA  is named a linear GSA [6] if the number of its operator vertices exceeds 75% of the total their number in the GSA.

Let the set  be constructed for GSA , where  is an operational linear chain (OLC) [6]. Any component  of OLC  belongs to the set  . Each pair of adjacent components ,  corresponds to the arc , where , . Each OLC  has only one output  and the arbitrary number of inputs. Formal definitions of OLC, its input and output can be found in [6]. Each vertex  corresponds to microinstruction  kept in the cell of control memory (CM) with address . It is enough

(1)

bits for microinstruction addressing, where . Let each OLC  include  components and . Let each OLC  be encoded by binary code  having

(2)

bits and variables  be used for such an encoding, where . Let each component  be encoded by binary code  having

(3)

bits and variables  be used for this encoding, where . The encoding of components is executed in such a manner that condition

(4)

takes place for each OLC  . If condition

(5)

takes place, then the model of CMCU with code sharing  can be used for interpretation of GSA  (Fig. 1).

Fig. 1. Structural diagram of CMCU U1

In CMCU , a block of microinstruction addressing (BMA) implements the system of input memory functions for counter CT and register RG:

(6)

Let us point out that in the case of CMCU  an address of microinstruction is represented as the following one:

,	(7)

where  is a component of OLC  and “*” is a sign of concatenation. The CMCU  operates in the following order.

If , then an initial address (all zeros) is loaded into RG and CT. In the same time a flip-flop TF is set up which causes , then microinstructions can be read out of control memory. Each cell of CM keeps microoperations  and special variables  and . If , then a current content of CT is incremented, otherwise both CT and RG are loaded from BMA. The first case corresponds to transition from any OLC component except of its output. The second case corresponds to transition from an OLC output. If , then the flip-flop TF is reset, signal  and operation of CMCU is terminated. It corresponds to transition from the vertex , where . Pulse Clock is used for timing of CMCU.

Let us point out that OLC  are pseudoequivalent OLC [6] if their outputs are connected with input of the same vertex of GSA . The hardware amount in logic circuit of BMA can be decreased due to introduction of a special block for transforming the OLC codes into the codes of the classes of pseudoequivalent OLC named as a code transformer (TC) [6]. But the TC consumes some resources of the chip in use.

In this article we propose to use free cells of CM for this transformation. To reduce the number of EMB in the control memory, we propose to use the maximum encoding of collections of microoperations [2].

3. Main idea of proposed method

Let  be a set of OLC such that their outputs are not connected with the vertex . Let us find the partition  of the set  by the classes of POLC. Let us encode classes  by binary codes  having  bits, where

.	(8)

Let us use variables  for this encoding, where .

In the process of CMCU synthesis, an initial GSA  is transformed and additional variables  and  are introduced in its operational vertices. Thus, the initial set  is transformed in the set . Let the set  includes  different collections of microoperations (CMO). Let us encode each collection  by a binary code  having  bits, where

.	(9)

Let us use variables  for this encoding, where . In this case the control memory includes two blocks [2], namely a block of micromemory (BMM) and a block of microoperations (BMO). The BMM generates functions

,	(10)

and the BMO generates variables

.	(11)

In this article we propose to include the fields  and  in the microinstruction format. These microinstructions include  bits, where

.	(12)

Both BMM and BMO are implemented using EMBs having  outputs. Assume that each EMB includes  words and

.	(13)

The block BMM has  outputs and it is implemented using  blocks EMB, where

.	(14)

In this case, there are  free bits in the word of BMM, where

.	(15)

These free bits can be used for keeping of some part  of the code .

All bits of  are generated by the BMM if the following condition takes place:

.	(16)

Otherwise, the block of code transformer (BCT) is used to generate the rest of the bits, , where

.	(17)

These bits form a part  of the code . This approach leads to a CMCU  (Fig. 2).

Fig. 2. Srtuctural diagram of CMCU U2

In CMCU , the block BMA implements functions

,	(18)

,	(19)

and the block BCT implements functions

.	(20)

The following conditions take places:

,	(21)

.	(22)

Functions of other blocks have been already discussed. Let us point out that logic circuits of BMA, CT, RG and TF are implemented using LUT elements, whereas circuits of BMM and BMO using EMBs. Logic circuits of BCT can be implemented using either LUT elements or EMBs.

In this article the following synthesis method is proposed for the CMCU :

- Construction of sets ,  and  for initial GSA .

- Encoding of OLCs, their components and classes.

- Encoding of collections of microoperations .

- Construction of control memory contents for blocks BMM and BMO.

- Construction of CMCU transition table.

- Construction of BCT table.

- Logic synthesis of CMCU logic circuit.

4. Application of proposed method

Let a GSA  be  represented by the sets , where , and , where , , ,  and . Content of  is:

,	,

,	,	,	,

, 	. Therefore, we can get the following values and sets: the number of OLC , for their encoding we use  variables from the set , maximum OLC length is  vertices, for their encoding  variables from the set  is enough, the number of operational vertices in the GSA ,  bits are necessary for their encoding. Hence, condition (5) takes place and there is possibility to use the code sharing. It is enough  variables for encoding of the classes . It means that .

Let us encode OLC  and their components in the following way: , …, , , …, . To satisfy the condition (4), let the first component of each OLC  have code 00, the second 01, the third 10, and the fourth 11. It leads to microinstruction addresses  shown in Table 1.

Table 1

Microinstruction addresses for CMCU U2(Г1)

| Address | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 00 |  |  |  |  |  |  |  |  |
| 01 |  |  |  |  |  |  |  |  |
| 10 |  |  | * |  |  |  | * |  |
| 11 | * |  | * | * |  | * | * | * |

From Table 1 we can derive, for example, that , , and so on. Replacement of vertices by corresponding collections of microoperations in Table 1 results in the content of control memory (Table 2).

Obviously, collections of microoperations are taken from the GSA , but we do not show it.

Table 2

Control memory content for CMCU U2(Г1)

| Address | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 00 |  |  |  |  |  |  |  |  |
| 01 |  |  |  |  |  |  |  |  |
| 10 |  |  | * |  |  |  | * |  |
| 11 | * |  | * | * |  | * | * | * |

As follows from Table 2, the control memory includes  collections of microoperations, namely: , , , , , , , . They can be encoded using  variables, therefore .

Let EMB in use have  outputs, then number of used EMB . Number of non-used bits . It means that one bit of the code  can be generated by the block BMM. Let variables  be devided between  and  in the following way: , .

It is enough to replace the collections in Table 1 by their codes to specify the block BMM. Each output of OLC  is complemented by value of the first bit of code . In our example, the block BMM is represented by Table 3, and the variable  is included in the output of OLC .

Table 3

Content of block BMM for CMCU U2(Г1)

| Address | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 00 | 000 | 001 | 000 | 011 | 100 | 000 | 100 | 001 |
| 01 | 001 | 011 | 101 | 100 | 001 | 011 | 110 | 100 |
| 10 | 010 | 100 | * | 110 | 000 | 010 | * | 111 |
| 11 | * | 110 | * | * | 101 | * | * | * |

The block BMO is specified by a table with columns , , . This table is constructed in a trivial way (Table 4).

Table 4

Content of block BMO for CMCU U2(Г1)

| 000 |  | 1 | 100 |  | 5 |
| --- | --- | --- | --- | --- | --- |
| 001 |  | 2 | 101 |  | 6 |
| 010 |  | 3 | 110 |  | 7 |
| 011 |  | 4 | 111 |  | 8 |

To construct the table of transitions for CMCU , it is necessary to construct the system of generalized formulae of transitions [6] for classes . Let the following system exist for our example:

(23)

Such a system is the base for construction of CMCU transition table including the following columns: , , , , , , , . The purpose of each column is clear from Table 5. The number of such a table rows  is determined by the number of terms in system of generalized formulae of transitions. In our case we have .

Table 5

Fragment of transitions table for CMCU U2(Г1)

|  | 010 |  | 10100 |  | – |  | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | 11000 |  | – |  | 7 |
|  |  |  | 10101 |  |  |  | 8 |

This fragment describes the transitions for class , starting from the sixth term of system (23). The table of transitions is used to derive functions (18)-(19), having the following terms

.	(24)

In system (24), the symbol  stands for value of the bit  of code  from the line  of the table: , ,  . For example, the following system can be derived from Table 5:

;

;

.

The table of BCT includes columns , , , , . In our example, Table 6 represents the block BCT.

Table 6

Specification of block BCT for CMCU U2(Г1)

|  | 000 |  | 000 | – | 1 |
| --- | --- | --- | --- | --- | --- |
|  | 001 |  | 001 |  | 2 |
|  | 010 |  | 001 |  | 3 |
|  | 011 |  | 010 |  | 4 |
|  | 100 |  | 010 |  | 5 |
|  | 101 |  | 011 |  | 6 |
|  | 110 |  | 100 | – | 7 |
|  | 111 |  | – | – | 8 |

Remind that the variable  is generated by the block BMM. In the same time, there is no code  because . Obviously, this table specifies blocks EMB. If the logic circuit of BCT is implemented using LUT elements, then Table 6 corresponds to Karnaugh maps for function . To optimize system (20), we should encode OLC  in the optimal way. The well-known method ESPRESSO [1], for example, can be used for such an encoding. We do not discuss this task in our article.

Implementation of the logic circuit of CMCU  is reduced to implementation of systems (18)-(19) using LUT elements, and tables similar to Table 3, Table 4, and Table 6 using EMB. To solve this task, a designer can use either standard tools [8,9] or some known methods [3]. We do not discuss this step also.

Let us point out that the control memory of CMCU  includes 32*12=384 bits (if ), and CMCU transition table includes 17 lines. In the CMCU , the BMM includes 32*4=128 bits, the BMO requires 8*11=88 bits, and the BCT consumes 8*2=16 bits. Therefore, the control memory of CMCU  uses 232 bits of memory, and its transition table has  lines. It means that the CMCU  requires 1.5 times less of the memory, and its block BMA includes 1.54 times less amount of terms.

5. Conclusion

In this article we propose the method oriented on hardware decrease in the logic circuit of CMCU. The method is based on including the field with code of class of pseudoequivalent OLC into the microinstruction format. The size of CMCU control memory is decreased too due to the maximal encoding of collections of microoperations. To decrease the number of LUT elements in the block of microinstruction addressing, the special code transformer is used. It transforms OLC codes into codes of their classes. This block can be absent if condition (16) takes place. In this case, the transformation is executed by CMCU block of  micromemory.

But such an approach leads to the CMCU   with less performance than this characteristic of CMCU with code sharing. Let us point out that reduction of the number of the LUT elements in logic circuit can result in decrease of its levels. It can compensate the negative effect of the memory splitting by two blocks. We made some examples of synthesis using the standard package WebPack. The results show that the number of LUT elements is decreased up to 30%, and the number of required memory blocks are decreased up to 50%. Comparison is given for CMCU  and . In the same time, the number of levels in logic circuit of CMCU  is decreased up to 2-3. Let us remind, that the proposed method can be applied only for linear GSA, when condition (5) takes place.

The scientific novelty of proposed method is determined by use of the classes of pseudoequivalent OLC and free resources of EMB for decreasing the number of LUT elements in block of microinstruction addressing. Besides, application of encoding of collections of microoperations allows decrease for required memory resources. The practical significance of the method is determined by decrease for the number of LUT elements and EMB in CMCU logic circuit, It allows to design the circuits with less amount of hardware in comparison with known control units oriented on linear GSAs.

References

- De Micheli G. Synthesis and Optimization of Digital Circuits. – NY: McGraw-Hill, 1994. – 636 pp.

- Barkalov A.A., Wegrzyn M. Design of Control Units with Programmable Logic. – Zielona Gora: UZG Press, 2006. –  150 pp.

- Maxfield C. The Design Warrior’s Guide for FPGAs – Amsterdam: Elsevier, 2004. – 514 pp.

- Solovjev V.V. Digital circuit design with CPLD. – Moscow: Hot Line-Telecom, 2001. – 636 pp. (in Russian).

- Sasao T. Switching Theory for Logic Synthesis. – Boston: Kluwer Academic Publishers, 1999. – 432 pp.

- Barkalov A., Titarenko L. Logic Synthesis for Compositional Microprogram Control Units – Berlin : Springer, 2008. – 272 pp.

- Baranov S. Logic Synthesis for Control Automata – Boston: Kluwer Academic Publishers, 1994 – 312 pp.

- Stratix IV Device Handbook // http://www.altera.com/literature/hb/stratix-iv/stratix4_handbook.pdf.

Virtex-5 FPGA Data Sheet: DC and Switching Characteristics // http://www.xilinx.com/support/documentation/data_sheets/ds202.pdf.